## Slide 1
A Comprehensive Summary
Chapter 9, Part 1
Inference Optimization

## Slide 2: The Physics of Inference: Compute vs. Bandwidth
The Roofline Model
Arithmetic Intensity: X-axis (FLOP/byte). Operations performed per byte of memory access.
Memory-Bound Region (Left): Performance is limited by data transfer speeds. Performance scales with Bandwidth.
Compute-Bound Region (Right): Performance is limited by arithmetic capability. Performance scales with FLOP/s.
Key Insight: LLM Decoding typically sits in the Memory-Bound region due to low arithmetic intensity.

## Slide 3: Terminology Ambiguity: Capacity vs. Bandwidth
Memory Capacity-Bound
Memory Bandwidth-Bound
Context: Hardware lacks sufficient RAM to store model weights or KV cache.
Symptom: "RuntimeError: CUDA out of memory" (OOM).
Mitigation: Split model across devices (Parallelism) or offload to CPU.
Context: Computation stalls waiting for data to travel from memory to compute units.
Symptom: High Latency. Low GPU Compute Utilization.
The Reality: In optimization literature (e.g. Roofline), "Memory-Bound" almost always refers to this bandwidth limitation.
Warning: Splitting models to solve Capacity issues often worsens Bandwidth issues due to slow device-to-device transfer.

## Slide 4: The Anatomy of Inference: Prefill and Decode
Parallel processing of input tokens. Compute-Bound. Creates the initial Key-Value (KV) cache.
Sequential generation (Autoregressive). Memory Bandwidth-Bound. Loads weights for each new token.
Optimization Implication: Decoupling these phases to different hardware instances prevents resource contention.

## Slide 5: Service Architecture: Online vs. Batch APIs

## Slide 6: Dissecting Latency: TTFT and TPOT
Total Latency = TTFT + (TPOT x Output Tokens)
Nuance: Chain-of-Thought (CoT) processes create 'invisible' latency before the first user-facing token appears.

## Slide 7: Throughput vs. Goodput: The SLO Reality Check
Throughput (TPS/RPS): Total tokens or requests processed per second. Can be inflated by aggressive batching at the cost of latency.
Goodput: The number of requests per second that satisfy the Service Level Objective (SLO).
Example Analysis: Reference the chart: If 10 requests are processed, but only 3 stay within the orange dashed lines (SLO), the Goodput is only 30% of the Throughput.
Goal: Maximize Goodput to balance cost efficiency with user experience.

## Slide 8: The Utilization Trap: Activity vs. Efficiency
GPU Utilization in standard tools measures the % of time the GPU is active, not how much work it is doing. A chip doing 1 operation per second is "100% Active" but "0% Efficient".
MFU (Model FLOP/s Utilization)
Ratio of observed throughput to theoretical peak FLOP/s.
Benchmark: Training > 50%; Inference is typically lower.
MBU (Model Bandwidth Utilization)
Ratio of observed memory bandwidth usage to theoretical peak bandwidth.
Relevance: The primary metric for decoding (memory-bound tasks).

## Slide 9: Calculating Model Bandwidth Utilization (MBU)
Worked Example: Llama 2-70B
Model Parameters: 70 Billion
Precision: FP16 (2 bytes per parameter)
Throughput: 100 tokens/sec
Hardware: NVIDIA A100 (Peak Bandwidth ~2000 GB/s)
Bandwidth Used: 70B * 2 * 100 = 700 GB/s
Result: MBU = 700 / 2000 = 35%
Insight: Reducing precision (Quantization) lowers the "Bytes/Param" factor, directly reducing bandwidth demand and improving performance.

## Slide 10: Al Accelerators: Specialized Hardware
Inference vs. Training Chips
Training Chips: Optimized for massive memory capacity (gradients/states) and high precision.
Inference Chips: Optimized for fast memory access (bandwidth), lower precision (INT8/FP8), and latency (e.g., AWS Inferentia, Google TPU, Meta MTIA).

## Slide 11: Computational Capabilities: FLOPs vs. FLOP/s
FLOPs (Plural)
Total floating-point operations required to complete a task.
Example: Training GPT-3-175B took ~3.14 x 10^23 FLOPs.
FLOP/s (Rate)
The speed of the hardware (Operations per Second).
Example: NVIDIA H100 Peak ~60 TeraFLOP/s.

## Slide 12: The Memory Hierarchy

## Slide 13: The Hidden Constraints: Power and Thermal Limits
TDP (Thermal Design Power)
Max heat a cooling system must dissipate.
e.g., H100 SXM = 700W.
Deployment Limits
Edge devices limited by battery. Data centers limited by grid availability and cooling infrastructure.
Efficiency Metric
Optimization Goal: Minimize Joules per Token.
Power is a hard physical constraint. High power density dictates where hardware can physically exist.

## Slide 14: Synthesis: The Inference Optimization Landscape

## Slide 15
In the next part, we will discuss
Model Compression
Autoregressive Bottleneck
Speculative Decoding
Parallel Decoding
The KV Cache Bottleneck
Writing Kernels
Inference Service Optimization
Decoupling & Prompt Caching
Parallelism Strategies
and much more…